## Slide 1: Real Time Wireless Drone’s Payload for Sampling Images and IMU Data
Dan Blanaru
Supervision: Mr. Yehonatan Mandel
Autonomous Drones Lab
Faculty of Electrical Engineering
Tel Aviv University
December 2020
https://github.com/tau-adl/Drones-Navigation-Payload

## Slide 2: Outline
Motivation
Project Goals
Approach
System Architecture
Design
Results
Other Project Products
Conclusion
Future Work
Acknowledgments

## Slide 3: Motivation
Growing demand for small autonomous platforms to preform indoor navigation or non-GPS based navigation1
Increasing interest in SLAM algorithms2
Lack of robust, flexible, generic, cheap and small form factor visual-inertial sensor3 for SLAM applications
1 https://bit.ly/3rGFPt9
2 https://yhoo.it/3ry0Bee
3 https://arxiv.org/pdf/1912.02469.pdf
Notes: רפאל מציגה: רחפנים שטסים בתוך מבנה ומזהים אם האנשים בו חמושים
התעניינות מצד ענקיות טכנולוגיה (גוגל, מייקרוסופט...) עם גידול שוק משמעותי
מאמר שסוקר בנייה של מצלמה מסונכרנת למדיד IMU, עם סטאפ יחסית גדול ומסורבל

## Slide 4: Project Goals
Creating visual-inertial sensor for drone’s payload that can send data wirelessly to a PC with low latency and real-time as possible
As implied from the goal above, the payload would be:
  Small form-factor (and lightweight)
  Minimal current consumption
  Standard wireless transceiver - Wi-Fi, BT, 900MHz dongle, etc.
  Data would be accurate to a 1msec timestamp precision
  Camera frame acquisition – RGB\ Grayscale, ~20fps
  IMU with 6DOF data
Communication with PC (Ubuntu\ Windows) and data integration with ROS framework

## Slide 5: Approach
Understanding the main key components of our system
Market Survey
Camera – better implement a Global Shutter technology
Communication – Wi-Fi presents more advantages vs BT (bandwidth, interface)
IMU – includes 3-axis accelerometer and 3-axis gyroscope
CPU (MCU) – should include interfaces to all peripherals and work in real-time

## Slide 6: System Architecture - Main Parts

## Slide 7: System Architecture

## Slide 8: Design
Steps:
  High-level design and product specifications
  Using open-source schematics, creating BSP and configuring interfaces from MCU to each periphery
  Utilizing drivers (both open-source and self-made) for each periphery
  POC tests and benchmarks
  Application utilization
  Tests and benchmarks

## Slide 9: Design – BSP (Schematics to BSP)
1 https://openmv.io/
1

## Slide 10: Design – Special MCU Internal Peripherals
DMA – Letting us transfer data efficiently between parts of the MCU
MPU – Manages transfer of data between different memory regions of the MCU
Timers – Creates system ‘heartbeat’ and synchronizes the different internal state machines and events
Communication interfaces – UART, I2C, SPI – for communicating between system parts
JPEG Encoder – Utilizing hardware periphery for compressing (and decompressing) JPEG images
DCMI – Dedicated Digital Camera Interface
SD – SD card + FATFS interface for saving images data locally

## Slide 11: Design – Application Architecture

## Slide 12: Design – Main Logic
Initialization
Initializes drivers and peripherals
Wait for Communication
Waits for ground station to request data
Main Loop
Acquire Image
Checks for peripheral health
Compress Image
Acquire IMU Samples
Send Data to Wi-Fi module

## Slide 13: Design – Init Phase

## Slide 14: Design – Heartbeat and System Phases
Notes: אירוע הטיימר מסנכרן את תחילת הצילום, לאחר מכן מיד מתחילה הדחיסה, והשליחה בעקבות סיום הדחיסה.
יש לדאוג לבניית תזמונים שלא גורמת לגלישה בפונקציונליות השליחה.

## Slide 15: Results
Development setup demo

## Slide 16: Results - Benchmark
Measurement setup
Typical FPS: 16fps
Resolution: 320x192, Grayscale
Results (our firmware) – ~10% better + sending IMU data
Results (existing OpenMV firmware example + chrome viewer):
delay |  |  |  | 
frames counted | average delay [msec] | stdev [msec] | max [msec] | min [msec]
16 | 237.50 | 27.73 | 270 | 200
delay |  |  |  | 
frames counted | average delay [msec] | stdev [msec] | max [msec] | min [msec]
16 | 266.25 | 32.19 | 360 | 230

## Slide 17: Other Project Products
A 3D printed casing was built1, system packed, and parts soldered
Verbose debug interface made for benchmark: displays 1msec accurate timestamp + events
1 https://www.thingiverse.com/thing:1656029

## Slide 18: Other Project Products - Continued
Ability to save input and output images of JPEG compressor – on SD card
Ubuntu eco-system burn & debug environment proof of concept for ADL’s purposes
Original
Compressed

## Slide 19: Other Project Products - Continued
Ground station live-view presentation of received image with benchmark

## Slide 20: Discussion & Conclusions
Understanding that the Wi-Fi module has limited capabilities made the image compression necessary
Implementing debug capabilities is integral part of the system architecture – both HW and FW
Using of-the-shelf products leads to fast prototyping, but users might need the ability to customize the product

## Slide 21: Future Work
Low-power modes for the system
Survey other transceivers for higher data rates - better resolution, less latency. Or varying the setup for current transceiver
Investigate the benefit for FLIR camera for the SLAM algorithms (the hardware supports it!)
Avoid fluorescent light flickering on camera
Utilizing USB debug interface
Dedicated system engineering – integrating all the parts on a single PCB, would lead smaller product, bring more robust HW

## Slide 22: Acknowledgments
Thanks to Mr. Yehonatan Mandel for supervising and guiding throughout the process with
Moreover, I must acknowledge my partner for implementing and designing other parts of this project that was not mentioned here, and was mentioned in his work summery – thanks to Shenhav Ovadia for collaborating and building this system with me on this project

## Slide 23: Thank You